Effect of Mechanical Index on Repeated Sparse Activation of Nanodroplets In Vivo

Ge Zhang1,2, Matthieu Toulemonde1, Kai Riemer1, Jiaqi Zhu1, Sevan Harput1,3, Kirsten Christensen-Jeffries4, Ziyan Zhu1, Bingxue Wang1, Chee Hau Leow1, Peter Weinberg1, Chris Dunsby5, Meng-Xing Tang1

1Ultrasound Lab for Imaging and Sensing, Department of Bioengineering, Imperial College London, London, UK

2Center for Ultrasound Research and Translation, Massachusetts General Hospital, Harvard Medical School, Boston, USA

3Division of Electrical and Electronic Engineering, London South Bank University, London, UK

4Biomedical Engineering Department, Kings College London, London, UK

5Department of Physics and Centre for Pathology, Imperial College London, London, UK

Email: Mengxing.Tang@Imperial.ac.uk

Abstract — Current localization-based super-resolution ultrasound imaging requires a low concentration of flowing microbubbles to visualize microvasculature beyond the diffraction limit and acquisition is slow. Previous studies have shown that sparse activation of nanodroplets can be used for generating fast or even real-time super-resolution imaging. However, the optimal experimental conditions to activate the droplets for generating the super-resolution images are still unknown, especially the activation ultrasound amplitude or mechanical index (MI). An in vivo super-resolution image of a rabbit kidney is obtained in 1.1 seconds using AWSALM pulse sequence. The aim of this study is to investigate the effect of the activation MI on the repeated activation of nanodroplets in the rabbit kidney. It was found that the droplet activation was not observed in the rabbit kidney at a MI of 1.1. The activation of droplet started at an activation MI of 1.3. The contrast of activated droplet signals is maximized at an MI of 1.5 and decreased when the activation MI was increased above 1.5. The possible explanation might be that, at high MIs, the activated droplets were destroyed. Such understanding of the effects of activation MI could help improve droplet-base fast super-resolution imaging.

Keywords— Super-Resolution, Decafluorobutane Nanodroplets, High Frame Rate, Flow Independent, Microbubbles

# Introduction

Ultrasound super-resolution imaging techniques have shown the capability of breaking the diffraction limit in spatial resolution [1-7]. However, these current localization-based ultrasound super-resolution imaging techniques rely on a low concentration of active flowing microbubble signals. This means that, for slow flows associated with the micro-vasculature, a longer acquisition time is required for the microbubbles to replenish. Therefore, there is a need to develop a super-resolution imaging technique to acquire images faster to facilitate the clinical translation.

Nanodroplets, also called ‘phase-change contrast agents’, have been widely investigated in the field of medical ultrasound imaging [8-10]. In contrast enhanced ultrasound imaging, there are three main advantages of using nanodroplets compared with the conventional microbubble contrast agents. First, the diameter of a nanodroplet is much smaller than a microbubble: previous theoretical work calculated that nanodroplets are 3-6 times smaller than microbubbles [11]. Their smaller size makes it possible for nanodroplets to flow into smaller vessels or extravasate into tumour tissue where microbubbles cannot. Second, the in vivo circulation time of nanodroplets has been shown to be at least 3-5 times longer than that of microbubbles [12]. This can potentially allow the scanning session to last longer and the nanodroplet dose to be smaller. Third, the nanodroplets can be manipulated/activated by an ultrasound pulse sequence at a specific time or spatial location to become microbubbles to provide contrast signals. This provides more control and flexibility to the real-time scanning.

The use of high and low boiling-point nanodroplets for super-resolution have been reported [8, 13]. The imaging of repeated activation and re-condensation of high-boiling-point perfluorohexane (boiling-point=56(C) nanodroplets can be used to generate super-resolution photoacoustic imaging. However, the optical activation of the high-boiling-point nanodroplets via laser pulses was required, which restricts its penetration depth to regions that can be illuminated optically.

An acoustic counter-part of optical localization microscopy [14, 15], which we called acoustic sparsely activated localization microscopy (AWSALM), has been proposed in our previous study which utilised low-boiling-point decafluorobutane (boiling-point=-2(C) nanodroplets.  AWSALM is a flow-independent technique and it does not require a low concentration of contrast agents. Compared to high-boiling-point nanodroplets, low-boiling-point nanodroplets have a much lower activation threshold and can be activated by diagnostic ultrasound pulses at depth.

Previous studies have shown AWSALM can be used to achieve super-resolution in vitro in a crossed-tube phantom. However, the optimal experimental conditions to activate the droplets for generating the super-resolution images are still unknown, especially the activation ultrasound amplitude or mechanical index (MI). The aim of this study is to investigate the effect of the activation MI on the repeated activation of nanodroplets in the rabbit kidney.

Fig. 1. Average of 1,000 SVD-filtered images of activated droplet signals acquired in 1 second as the activation MI increases.

# Methods and Experiment

## Nanodroplet Preparation

The preparation of the nanodroplet solution has been adapted from previously described methods [16-19]. The lipid shell was generated by dissolving 1,2-dipalmitoyl-sn-glycero-3-phosphocholine (DPPC) and 1,2-distearoyl-sn-glycero-3-phosphoethanolamine-N-[amino(polyethylene glycol)-2000] (DSPE-PEG-2000) into a solution of phosphate-buffered saline (PBS), propylene glycol, and glycerol. All the lipids described above were purchased from Avanti Polar Lipids, Inc., USA. The lipid solution was added to a glass vial and the headspace of vial was exchanged with decafluorobutane gas (Fluoromed, USA) via an inlet needle along with a vent needle. Mechanical agitation was sufficient to produce the formation of lipid-shell octafluoropropane-core microbubbles. In order to condense microbubbles into nanodroplets, the headspace of the vial was pressurised while the vial immersed in the ice-water bath according to the previously described method [20-24].

## Animal Preparation

A specific pathogen-free male New Zealand rabbit (HSDIF strain; Envigo, Hillcrest, United Kingdom) was used in this study and all animal experiments complied with the Animals (Scientific Procedures) Act 1986 and were approved by the local ethical review panel. The rabbit was aged 8 weeks and individually housed in pens at 18 – 22 ℃ on a 12-hour light period and was fed a standard laboratory diet.

## In Vivo Protocol

Fentanyl and fluanisone (0.3 mL/kg) and midazolam (0.025 mL/kg) were administered through the marginal vein of each rabbit to produce general anesthesia. Maintenance doses were given as required. The rabbit was placed on a warming pad to maintain body temperature at 37 ℃ and artificially ventilated. A 0.4 mL intravenous bolus of concentrated decafluorobutane nanodroplets (10^10 droplets/mL) were injected in the rabbit prior to ultrasound scanning of the rabbit kidney.

## Image Acquisition

A customised ‘Imaging – Activation - Imaging’ sequence  [25-28] was implemented on an ultrasound research platform (Verasonics Vantage 128, Kirkland, USA) with a L11-4 38-mm linear array probe (ATL, USA). Focused pulses were transmitted to activate the nanodroplets and interleaved with plane waves (MI =0 .25, frame rate = 1000 Hz) for imaging with a transmit frequency of 3.5 MHz. 1000 images were acquired over 1.1 seconds (1.0 s imaging time + 0.1 s activation time). The acquisition was repeated with different activation MIs (MI=1.1, 1.3, 1.5, 1.7, and 1.9).

## Image Analysis

Singular value decomposition (SVD) processing was used to separate the activated nanodroplet (i.e. microbubble) signal by removing the background. The SVD thresholds were automatically determined from the location of the largest gradient on the energy versus singular value order curve. [8]. After SVD processing, the averaged images were displayed and the contrast within the region of interest was quantified.

# RESULTS AND DISCUSSIONS

Fig 1 shows the average of 1000 SVD-filtered image frames acquired in 1.1 s with the different activation MIs ranged from 1.1 - 1.9. It can be seen that, the droplet activation was not observed in the rabbit kidney at a MI of 1.1. The activation of droplet started at an activation MI of 1.3.

Fig. 2. Quantification of normalized contrast within the region of interest (indicated by the red boxes outlined in Fig. 1).

Fig 2 shows the quantification of normalized contrast within the region of interest indicated by the red boxes outlined in Fig.1. The contrast of activated droplet signals is maximized at an MI of 1.5 and decreased when the activation MI was increased above 1.5. The possible explanation might be that, at high MIs, the activated droplets were destroyed.

# CONCLUSION

##### In summary, this study investigates the effect of the activation MI on the repeated activation of nanodroplets in the rabbit kidney. The images were obtained in 1.1 seconds using AWSALM pulse sequence. The activation MI of the transmitted pulses was controlled within the FDA-approved safety range (MI<1.9). The results suggest that, a medium MI is preferred while the droplets are repeated activated and imaged. The possible explanation for this might be that, the droplets could not be activated at a low MI level and droplets would be destroyed by repeated activation pulses at a high MI level. Such understanding of the effect of activation MI could help improve the droplet-base fast super-resolution imaging.

##### Acknowledgment

##### This work was supported by the EPSRC under Grant EP/N015487/1 and EP/N014855/1, in part by the King's College London (KCL) and Imperial College London EPSRC Centre for Doctoral Training in Medical Imaging (EP/L015226/1), in part by the Wellcome EPSRC Centre for Medical Engineering at KCL (WT 203148/Z/16/Z), in part by the Department of Health through the National Institute for Health Research comprehensive Biomedical Research Center Award to Guy's and St Thomas' NHS Foundation Trust in partnership with KCL and King's College Hospital NHS Foundation Trust, in part by the Graham-Dixon Foundation and in part by NVIDIA GPU grant. This work is also supported by the CRUK Multidisciplinary Project Award (No. C53470/A22353), and Imperial-ICR CRCE pump-priming awards.

##### References

1.	Viessmann, O.M., et al., Acoustic super-resolution with ultrasound and microbubbles. Phys Med Biol, 2013. 58(18): p. 6447-58.

2.	Christensen-Jeffries, K., et al., 3-D In Vitro Acoustic Super-Resolution and Super-Resolved Velocity Mapping Using Microbubbles. IEEE Trans Ultrason, Ferroelectr, Freq Control, 2017. 64: p. 1478-1486.

3.	Christensen-Jeffries, K., et al., In Vivo Acoustic Super-Resolution and Super-Resolved Velocity Mapping Using Microbubbles. Ieee Transactions on Medical Imaging, 2015. 34(2): p. 433-440.

4.	Lin, F., et al., 3-D Ultrasound Localization Microscopy for Identifying Microvascular Morphology Features of Tumor Angiogenesis at a Resolution Beyond the Diffraction Limit of Conventional Ultrasound. Theranostics, 2017. 7(1): p. 196-204.

5.	Errico, C., et al., Ultrafast ultrasound localization microscopy for deep super-resolution vascular imaging. Nature, 2015. 527(7579): p. 499-502.

6.	Couture, O., et al., Ultrasound Localization Microscopy and Super-Resolution: A State of the Art. IEEE Transactions on Ultrasonics, Ferroelectrics, and Frequency Control, 2018. 65(8): p. 1304-1320.

7.	Song, P., et al., Improved Super-Resolution Ultrasound Microvessel Imaging with Spatiotemporal Nonlocal Means Filtering and Bipartite Graph-Based Microbubble Tracking. IEEE transactions on ultrasonics, ferroelectrics, and frequency control, 2018. 65(2): p. 149-167.

8.	Zhang, G., et al., Acoustic wave sparsely activated localization microscopy (AWSALM): Super-resolution ultrasound imaging using acoustic activation and deactivation of nanodroplets. Applied Physics Letters, 2018. 113(1): p. 014101.

9.	Zhang, G., et al. Investigation of Nanodroplet Adhesion to Endothelial Cells under Atheroprone Flow Conditions in 2018 IEEE International Ultrasonics Symposium (IUS). 2018.

10.	Toulemonde, M., et al. Flow Visualization through Locally Activated Nanodroplets and High Frame Rate Imaging. in 2018 IEEE International Ultrasonics Symposium (IUS). 2018.

11.	Sheeran, P.S., et al., Methods of Generating Sub-Micron Phase-Shift Perfluorocarbon Droplets for Applications in Medical Ultrasonography. IEEE Trans Ultrason Ferroelectr Freq Control, 2016.

12.	Sheeran, P.S., et al., Contrast-enhanced ultrasound imaging and in vivo circulatory kinetics with low-boiling-point nanoscale phase-change perfluorocarbon agents. Ultrasound Med Biol, 2015. 41(3): p. 814-31.

13.	Luke, G.P., A.S. Hannah, and S.Y. Emelianov, Super-Resolution Ultrasound Imaging in Vivo with Transient Laser-Activated Nanodroplets. Nano Lett, 2016. 16(4): p. 2556-9.

14.	Dudok, B., et al., Cell-specific STORM super-resolution imaging reveals nanoscale organization of cannabinoid signaling. Nat Neurosci, 2015. 18(1): p. 75-86.

15.	Betzig, E., et al., Imaging Intracellular Fluorescent Proteins at Nanometer Resolution. Science, 2006. 313: p. 1643-1645.

16.	Lin, S., et al., Imaging of vaporised sub-micron phase change contrast agents with high frame rate ultrasound and optics. Physics in Medicine and Biology, 2018.

17.	Lin, S., et al., Effects of microchannel confinement on acoustic vaporisation of ultrasound phase change contrast agents. Physics in Medicine & Biology, 2017. 62(17): p. 6884.

18.	Zhang, G., et al., Fast Acoustic Wave Sparsely Activated Localization Microscopy: Ultrasound Super-Resolution Using Plane-Wave Activation of Nanodroplets. IEEE Transactions on Ultrasonics, Ferroelectrics, and Frequency Control, 2019. 66(6): p. 1039-1046.

19.	Zhang, G., et al. Contrast-Enhanced Photoacoustic Imaging of Low-boiling-point Phase-Change Nanodroplets. in 2019 IEEE International Ultrasonics Symposium (IUS). 2019.

20.	Zhang, G., et al. Acoustic response of targeted nanodroplets post-activation using high frame rate imaging. in 2017 IEEE International Ultrasonics Symposium (IUS). 2017.

21.	Zhang, G., et al., Quantification of Vaporised Targeted Nanodroplets Using High-Frame-Rate Ultrasound and Optics. Ultrasound in Medicine & Biology, 2019. 45(5): p. 1131-1142.

22.	Zhang, G., et al. Acoustic Wave Sparsely-Activated Localization Microscopy (AWSALM): A Fast and Flow Independent Ultrasound Super-Resolution Technique using Nanodroplets. in 2018 IEEE International Ultrasonics Symposium (IUS). 2018.

23.	Zhang, G., et al. High Signal-to-Noise Ratio Contrast-Enhanced Photoacoustic Imaging using Acoustic Sub-Aperture Processing and Spatiotemporal Filtering. in 2019 IEEE International Ultrasonics Symposium (IUS). 2019.

24.	Zhang, G., et al. Photoacoustic Super-Resolution Imaging using Laser Activation of Low-Boiling-Point Dye-Coated Nanodroplets in vitro and in vivo. in 2019 IEEE International Ultrasonics Symposium (IUS). 2019.

25.	Lin, S., et al. Vaporising phase change ultrasound contrast agent in microvascular confinement. in 2016 IEEE International Ultrasonics Symposium (IUS). 2016.

26.	Zhang, G., et al. Super-Localisation Ultrasound Imaging using Sparse Activation of Low-Boiling-Point Nanodroplets. in The 23rd European Symposium on Ultrasound Contrast Imaging. 2018. Rotterdam, Netherlands.

27.	Lin, S., et al. High frame rate ultrasound imaging of vaporised phase change contrast agents. in 2017 IEEE International Ultrasonics Symposium (IUS). 2017.

28.	Zhang, G., et al. Minimization of Nanodroplet Activation Time using Focused-Pulses for Droplet-Based Ultrasound Super-Resolution Imaging. in 2019 IEEE International Ultrasonics Symposium (IUS). 2019.